## Slide 2: Cisco Networking Academy
Networking
CCNA Security
Introductory
Advanced
Cisco CCENT
Cisco CCNA R&S
Cisco CCNA Security
Cisco CCNP
CCNA R&S 1 Introducing to Networks
CCNA R&S 2 Routing and Switching Essentials
CCNA R&S 3 Scaling Networks
CCNA R&S 4 Connecting Networks
CCNP Switch
CCNP Route
CCNP TShoot
Cisco CCNP Security

## Slide 3: Mod de desfasurare
Networking
CCNA Security
Introductory
Advanced
CCNA R&S 1 Introducing to Networks
CCNA R&S 2 Routing and Switching Essentials
CCNA R&S 3 Scaling Networks
CCNA R&S 4 Connecting Networks
CCNP Switch
CCNP Route
CCNP TShoot
11 sedinte de 4 ore
10 sedinte de 4 ore
10 sedinte de 4 ore
8 sedinte de 4 ore
10 sedinte de 4 ore
10 sedinte de 4 ore
10 sedinte de 4 ore
10 sedinte de 4 ore
Sedinta: Teorie + Laborator
CCNA R&S 1: 50% + 50%
CCNA R&S 2: 20% + 80%
CCNA R&S 3: 20% + 80%
...

## Slide 4: Reguli de promovare CCNA 1
Examene la capitole
Prezenta 7 din 11
Evaluare practica
Examen final

## Slide 5: Adresare IP
10 . 1 . 0 .100
255.255. 0 . 0
IP uri in total : 10.1.0.0 – 10.1.255.255
IP uri folosibile: 10.1.0.1 – 10.1.255.254

## Slide 6: SOHO Router AP
Route+Switch+Access Point

## Slide 7: SOHO Router AP
Route+Switch+Access Point

## Slide 8: Routerul Separa Retelele si Ofera Servicii

## Slide 9: Scenariul 1. Home Office

## Slide 10: Scenariul 2. Small Office

## Slide 11: Configurare Scenariu AP

## Slide 12: Transformari Binar-Zecimal-Hexazecimal
Binar > Zecimal
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 13: Transformari Binar-Zecimal-Hexazecimal
Binar > Zecimal
1 1 1 0 0 0 1 1
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 14: Transformari Binar-Zecimal-Hexazecimal
Binar > Zecimal
1 1 1 0 0 0 1 1
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
225

## Slide 15: Transformari Binar-Zecimal-Hexazecimal
Binar > Zecimal
0 1 0 1 0 1 1 0
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 16: Transformari Binar-Zecimal-Hexazecimal
Binar > Zecimal
0 1 0 1 0 1 1 0
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
86

## Slide 17: Transformari Binar-Zecimal-Hexazecimal
Binar > Zecimal
1 0 1 0 0 1 0 1
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 18: Transformari Binar-Zecimal-Hexazecimal
Binar > Zecimal
1 0 1 0 0 1 0 1
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
165

## Slide 19: Transformari Binar-Zecimal-Hexazecimal
Binar < Zecimal
201 – 128 = 73
1
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 20: Transformari Binar-Zecimal-Hexazecimal
Binar < Zecimal
201-128 = 73-64=9
1 1
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 21: Transformari Binar-Zecimal-Hexazecimal
Binar < Zecimal
201-128 = 73-64=9
1 1 0 0
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 22: Transformari Binar-Zecimal-Hexazecimal
Binar < Zecimal
201-128 = 73-64=9-8 =1-1
1 1 0 0 1 0 0 1
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 23: Transformari Binar-Zecimal-Hexazecimal
Binar < Zecimal
150=128+16+4+2
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 24: Transformari Binar-Zecimal-Hexazecimal
Binar < Zecimal
150=128+16+4+2
1 0 0 1 0 1 1 0
___ ___ ___ ___ ___ ___ ___ ___
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 25: Transformari Binar-Zecimal-Hexazecimal
3. Binar > Hexazecimal
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 26: Transformari Binar-Zecimal-Hexazecimal
3. Binar > Hexazecimal
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 27: Transformari Binar-Zecimal-Hexazecimal
3. Binar > Hexazecimal
4. Binar < Hexazecimal
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 28: Transformari Binar-Zecimal-Hexazecimal
3. Binar > Hexazecimal
4. Binar < Hexazecimal
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 29: Transformari Binar-Zecimal-Hexazecimal
5. Zecimal >Binar > Hexazecimal
100
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 30: Transformari Binar-Zecimal-Hexazecimal
5. Zecimal >Binar > Hexazecimal
100=64+32+4
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 31: Transformari Binar-Zecimal-Hexazecimal
5. Zecimal >Binar > Hexazecimal
100=64+32+4
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 32: Transformari Binar-Zecimal-Hexazecimal
5. Zecimal >Binar > Hexazecimal
100=64+32+4
6. Zecimal<Binar < Hexazecimal
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 33: Transformari Binar-Zecimal-Hexazecimal
5. Zecimal >Binar > Hexazecimal
100=64+32+4
6. Zecimal<Binar < Hexazecimal
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 34: Transformari Binar-Zecimal-Hexazecimal
5. Zecimal >Binar > Hexazecimal
100=64+32+4
6. Zecimal<Binar < Hexazecimal
128+64+4=196
Deci | Heza | Binar
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 35: Tema Curs 1